## Slide 1: Starting a campground

## Slide 2: objectives
Partner with WACO to develop this presentation
Help operators navigate licensing process
Provide resources

## Slide 3: timeline
Zoning-months
Licensing
Variances-30 days
  Sanitary stations
Planning and Organization will help you
License application will guide you

## Slide 4: Not always a completely linear process

## Slide 5: Different scenarios: licensing
Change in owner only
  License application
Same owner, expansion to new license category
  License application

## Slide 6: Different scenarios: plan review
New owner, new campground or expanding what is there
  Plan review
Same owner, any expansion (adding or changing type of attributes)
  Plan review

## Slide 7: Quick terminology review
Attribute: water distribution, toilet building, operator-provided camping unit, campsite
Independent Camping Unit/Campsite: tanks for wastewater and potable water
Dependent Camping Unit/Campsite: no toilet on-board
New campsite: created on or after February 1, 2016

## Slide 8: What’s the purpose of a plan review
Provide guidance towards compliance at a time when changes can more easily be made
Provide heads-up for something that may not work long-term (capacity)
Provide code interpretation specific to proposed campground or expansion
Help campground operator avoid building something that cannot meet the code

## Slide 9: What will always be true
Campsites: existing campsites (pre-Feb 1, 2016)
  ‘old code’ applies
For new campsites
  Separation between campsites
  Fire rings (distances)
  Campsite marking

## Slide 10: For Any NEW construction
Campsites in a floodplain?
  County zoning or DNR
  Avoid headaches
Is any new entrance safe?
  Traffic
Licensed plumber
Will well and septic be possible
Number of campsites (separation)

## Slide 11: What is the first thing I should do?
Health inspector
  Plan review and/or licensing guidance

## Slide 12: What is the other first thing I should do?
Check with County
  Zoning approvals and other inspections
    Use of property and location
    Buildings
    Plumbing
  Campsites in floodplain (might be DNR)

## Slide 13: What should I do next
What are my options for the entrance, if there will be a new entrance?
  Large trucks and RVs (turning radius)
  Slow acceleration onto highway
  Highway departments

## Slide 14: Next: water
If well needed, is a well possible?
Connections at the campsites?
  T’s
Approved distribution systems
  No buried-hose systems
Tap for Dependent campsites?
High-capacity well? (peak demand)

## Slide 15: Powts: what are options?
Capacity considerations
  Central (one large or multiple?) or stand-alone
  Work with soil tester
  Plan out 10 years (future capacity)
  Any houses
  Toilets and showers
  Campsites
  Sanitary station (or future sanitary station)

## Slide 17: What is happening with waste water?
All Dependent
  Install toilets
All with at least RV transfer tanks
  No sanitary station required
  Plan for disposal (on-site or contractor)
All with sewer connection
  No sanitary station and no back up toilets required

## Slide 18: When do I need to meet minimum number of toilets?
If any campsites designated Dependent

## Slide 19: When do I need 2 back-up toilets?
Whenever an Independent campsite is not connected to a sewer
  RV transfer tank does not count here (capacity)
  Male/female fine

## Slide 20: When do I need a sanitary station
Independent campsites without RV transfer tank or sewer connection
Variance can take 30 days (start early)
  Variance available for 20 or fewer
  Sanitary station must be within 25 miles/agreement
    State parks, municipal, truck stops

## Slide 21: SO far so good? If adding water or sewer
Licensed plumber
  Will work with relevant agencies
  Plumber submits plans to relevant agencies

## Slide 22: DSPS issues Conditional approvals
Water lines
  To campsites
  Within 400 feet of any Dependent
Sewer
  For toilets
  For campsite
Septic
Sanitary station

## Slide 23: Zoning issues sanitary permit
They inspect at installation
Will send maintenance notices

## Slide 24: At this point you should know
What the county requires (DSPS)
What the DNR will require (well, flood plain)
Ponds?
If you need a toilets or a sanitary station

## Slide 25: (Later on, After well constructed)
You’ll need a ‘successful’ well construction report
  No problems reported by driller to DNR
‘Safe’ water sample

## Slide 26: Next step: Draw your map
It can be to-scale or
You can just write in distances
  Dependent campsites to toilets
  Dependent campsites to water
  Any campsites to sanitary station
  Camping unit to camping unit likely distance
Limit guest exposure to wells/POWTS

## Slide 27: A few examples
Architect drawing to-scale
Any clear drawing with distances and attributes noted

## Slide 28: This one would be simple and quick to review

## Slide 30: Other drawings we have worked with

## Slide 31: Needed to know about scale or distances for this otherwise very clear drawing
Sometimes this is in an accompanying document
If possible, put on main drawing (speeds up review)
Consider size of rig at this point (pull-throughs)
Traffic direction

## Slide 33: This one was an expansion
Additional information provided earlier (phases 1 and 2)
Distances for new Independent sites noted at top
Distances (width with RV, deck, shed)

## Slide 35: Note distances indicated here for these independent units
Turning radius
One-way
Distances

## Slide 37: This next one needs work to help us understand what will be in place

## Slide 39: This one needed a little work on water and toilets, all sites dependent

## Slide 41: When you have your drawing(s)
Complete the plan review application
Compile approvals
If any reports or approvals are pending, let reviewer know
Include the drawing
Submit your plans to your inspector or DATCP plan reviewer
  For DATCP if unsure, ask your inspector as they do some expansion reviews

## Slide 43: Well documents
Driller provides report to DNR
If problem DNR notifies driller and owner
Time period given for correction
DNR also conducts site visits
Sampling upon completion

## Slide 48: Send it all in to reviewer
Compile what you have
Plans are reviewed
More information may be requested

## Slide 49: reviewer
At DATCP (State-inspected areas)
  New campground: Mary Ellen Bruesch or Ted Tuchalski
  DATCPDFRS REC@wisconsin.gov
  Expansions, work with your inspector
Agent inspected areas, work with inspectors

## Slide 50: Plan approval example

## Slide 51: Licensing inspection
Verify plans
Review documents
Release license if appropriate

## Slide 52: licensing

## Slide 53: Helpful websites
DATCP Licensing
https://datcp.wi.gov/Pages/Licenses_Permits/FoodRecLicenseGeneral.aspx
DATCP Campgrounds
https://datcp.wi.gov/Pages/Programs_Services/Campgrounds.aspx
DSPS plumbing products (RV transfer tanks)
https://apps3.dsps.wi.gov/php/sb-ppalopp/prodcode_result.php/STRVTC/SEWAGE_TANKS,_RV_TRANSFER_TANK
DNR Floodplain contacts
https://dnr.wi.gov/topic/FloodPlains/staff_flood.html
Wisconsin sanitary stations
https://www.rvdumps.com/wisconsin/
DATCP Resources
Maryellen.Bruesch@wisconsin.gov

## Slide 54: In conclusion
Learned about navigating planning and licensing process